I.	Scope of Services

Services to complete a Statistical Sample Tree Inventory of the (Community Name) properties as specified in this document. If these services and terms are acceptable, this document will serve as a contract for services.

II.	Sample Tree Inventory

The objective is to complete a 3-6% random sample inventory of trees located along community streets, on parklands and other public properties defined in the following:

- Inventory Methodology

- Street Trees

  - Sample 3-6% of street miles

  - Stratification

    - Minimum – 4 quadrants

    - Zoning districts or other

  - Sample units are street block segments.

  - Inventory all trees and planting sites on the sample block segment

- Park Trees & Public Property

  - 3-6% of the property area

  - Stratification

    - Mowed areas

    - Natural areas

- Standard Error

  - <=10%

B.	Scope of Inventory – Walk each street sample plot and walk each property sample plot, and identify trees as specified, catalogue tree management and location information for these trees and make management recommendations as specified.

- Trees that will be inventoried

  - All trees and street tree planting sites

  - Street Trees

    - All trees and planting sites located within the street right of way (ROW).

    - The (Community Name) will provide the ROW widths for each street, definition of the ROW and /or manpower to identify the ROW.

  - Park/Properties

    - Trees located within high target areas and intensively managed landscaped properties.  These will include:

      - Properties that have a high frequency of pedestrians, traffic, parking, buildings and the landscapes that are mowed.

    - The margins of the above referenced properties that are either naturalized or bordering adjacent property owners

    - The (Community Name) will define the scope of the area to be surveyed including survey maps, property limits and or the manpower to define the properties to be surveyed.

B.	Level of Inspection and Defining Management Recommendations

1.   Level of Inspection – The base fee shall include a Level 1 Limited Visual Assessment as defined by the International Society of Arboriculture’s (ISA) BMP plus work prioritization.

a.   Level 1 Limited Visual Assessment – A visual inspection of trees on the (Community Name) property to identify trees with visible obvious tree defects. Trees with defects that warrant management action will receive a walkaround inspection and sounding, a management recommendation (Work Need) as well as recommendation for further assessment if the tree warrants and collection of the tree inventory information detailed below in section C.

- Management Recommendations – Management recommendations for each tree inventoried are defined as follows:

  - Tree Removals

    - Trees with readily obvious, major defects that present an unacceptable risk of failure under normal weather conditions will be considered for removal. The tree’s health and the severity of the defects present will be considered when making a removal recommendation. If one-third or more of a tree’s live must be removed to remove defective limbs, the tree will be recommended for removal.

  - Pruning Needs

    - Safety Prune

      - Defective branches 4 inches in diameter or larger

      - Branches over street being struck by vehicles

      - Branches hanging into sight line of pedestrians over sidewalks

      - Branches resting on street lights, other structures or utilities

      - These needs will be prioritized.

    - Reduction prune – tree with trunk or large scaffold defects that require reduction pruning to reduce the risk of failure

    - Routine Prune – tree to be pruned during routine pruning schedules

    - Train Prune – young tree requiring structural train pruning

    - Planting Sites (Streets Only)

C.	Tree Management Data Variables – The following data will be collected for each tree:

- Tree Data

  - Street or Park/Property Name

  - Address

  - On street – Street Trees Only. Street the tree is located on.

  - Tree number. Park trees will be the tree tag number attached to each tree.

  - Side of Lot – front, side rear or median, north, east, south, west

  - Tree genus, species and common name – each tree will be identified to genus and species, and a common name will be provided.

  - DBH (diameter breast height) – Diameter in inches at 4 ½ feet above grade measured with a diameter tape or Biltmore stick

  - Tree Height – estimated in feet

  - Tree Spread – estimated in feet

  - Management or Work Need – as described in (II) above

  - Management Priority – each tree will be assigned a management priority based on the targets present, frequency and consequences of failure

    - Highest

    - Medium

    - Lowest

    - None

  - Health – Tree Biological Health or the condition of foliage and twigs expressed as:

    - Excellent – exceptional shoot growth, foliar color and density, and absence of dieback or damaging pests

    - Good – typical condition for the species including shoot growth, foliar color and density, and absence of dieback or damaging pests

    - Fair – deficiency in one category such as below normal shoot growth, foliar color and density, or presence of dieback or damaging pests

    - Poor – below typical or deficiency in two or more categories such as shoot growth, foliar color and density, or presence of dieback or damaging pests

    - Very Poor – major deficiency in two or more categories such as shoot growth, foliar color and density, or presence of major dieback or damaging pests

    - Dead – no living tissues

  - Structure – Tree structure or the condition of structural portions of the tree, expressed as:

    - Excellent – exceptional structure with an absence of any structural defects such as decay or weak branch attachments

    - Good – absence of any significant structural defects although minor defects such as low amounts of decay that are unlikely to fail under normal weather conditions may be present

    - Fair – one significant structural defect is present that may fail under storm conditions, or several minor structural defects can be found.

    - Poor – one or more significant structural defects are present that may fail under normal weather conditions.

    - Very Poor – several significant structural defects are present that may fail under normal weather conditions.

  - Overhead utilities – presence of primary or secondary electrical distribution wires or telephone or street lighting

  - Site Type – type of location the tree is growing in such as lawn area, natural area, border tree, tree lawn, street median or tree pit

  - Planting Area – Most limiting dimension of planting area in feet

  - GPS Coordinates

D	Quality Control – the following quality control checks will be implemented during the inventory:

- All data will be reviewed digitally for errors, and errors will be corrected.

- One percent of the inventory will be randomly reinspected in the field for error. Most re-evaluations will focus on the trees recommended for removal.

E	Data Format

- Excel spreadsheet with all data

- Shape file

F. 	Inventory Report

1.  An inventory report summarizing the data collected and methods used will be provided.

  - Fee Schedule

| Item | Fee |  |  |  |
| --- | --- | --- | --- | --- |
|  | Street Trees | Park Trees | Public Properties | Total |
| 3% Sample – Community Population > 250,000 |  |  |  |  |
| 4% Sample – Community Population 150,00 - 250,000 |  |  |  |  |
| 5% Sample – Community Population 50,000 – 150,000 |  |  |  |  |
| 6% Sample – Community Population < 50,000 |  |  |  |  |

    - Contract Requirements

Qualifications

Company/Firm

The company must demonstrate in a brief narrative and at least five (5) years of experience in completing municipal address-based and GPS tree inventories. Please supply three references. 

Inventory Staff

Staff performing the field inventory work must have the following minimum qualifications. Provide a list of their names and qualifications.

- An associate degree in Arboriculture or Urban Forestry or an International Society of Arboriculture Certified Arborist and three (3) years experience completing municipal tree inventories.

- International Society of Arboriculture Tree Risk Assessment Qualified